## Slide 1: 5th Generation Wireless – where is that going and what’s in it for me?
Jurui Qi
Prof. Gabriel M. Rebeiz
ECE Department
University of California, San Diego
La Jolla, CA 92093-0407
12-18-2024
3-6 GHz Dual-pol Reconfigurable Intelligent Surface
(RIS) Interface Control Document

## Slide 2: Content of ICD
Part 1: RIS Board, Mechanical, RF/Electrical Specs
Part 2: 3-6 GHz RIS Control
Appendix: 2x2 Feed Array Specs
Attached:
  RIS Holder 3D STEP Files
  MATLAB Control Files

## Slide 3
Part 1: RIS Board, Mechanical, RF/Electrical Specs

## Slide 4
RIS System Block Diagram
Arduino
Due
VCC
GND
USB
Digital I/O
Array Area

## Slide 5: RIS System Block Diagram: System View
The boards are ESD sensitive, please use ESD strap when handling the array
Array Front View
Array Back View
Array Area
V-pol
H-pol
SP4T & PS
Power & Digital Controls
39.7 cm
31.5 cm
39.7 cm
31.5 cm

## Slide 6: RIS System Block Diagram: System View
VCC (5V)
Banana
Cables
GND
USB
GND
VCC
Array Area
Board Name: 3-6 GHz TTD Reflectarray Feed
Board size: 31.5 x 39.7 cm
144 elements planar antenna array with 2.5 cm spacing: (0.5λ @ 6GHz)
Stacked patch antenna with S11 bandwidth from 3-6GHz
The RIS is powered and controlled by the DC/Digital pins with Arduino Due microcontroller
3mm 3D-printed spacer
1.35mm 3D-printed spacer
Array Side View
Upper Patch Board
Lower Patch Board
Feed Board

## Slide 7
3-6 GHz RIS: Voltage & Current Consumption
Power consumption of 3-6 GHz RIS
This is at regular setting. Current consumption can vary slightly depending on the states and
VCC | Current
5V | 0.05 A
Absolute Maximum Ratings
Voltage | Current | Total Power Consumption
VCC (5V) | 0.035 A | 0.18 W

## Slide 8: 3-6 GHz RIS: RF Performance
RIS Performance Summary |  | 
Parameter | Value | Comment
Frequency Range | 3-6 GHz | Operational BW
Scanning Range (Deg.) | +/- 60o | @ 3-6 GHz
Sidelobe level | <-10 dB | Focal and Planewave Feed

## Slide 9
Part 2: 3-6 GHz RIS Control

## Slide 10: 3-6 GHz RIS: Control Configuration
Arduino
Due
VCC
GND
USB
Digital I/O
Every two antennas are considered as one element in control
For each element, an 8-digit state code is required to set phase shifter
Another 11-digit is required to select which element is going to be set
All digital IO are using Arduino Due
All codes are written in MATLAB and require the MATLAB Arduino connected IO support package
Array Front View
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
69
70
71
72
68
67
General Control Schematic
A. Send 8-digit state code (function: set_latch() )
B. Enable the selected element to implement the state code (function: pulse_decoder() )
C. Redo above steps for another element
Example control code
for n=1:72 %go through all 72 elements
set_latch(Ard_obj, state_code_dec) %8-digit state code to set PS
pulse_decoder(Ard_obj, n) %enable corresponding element to implement
end

## Slide 11: Digital Control Components
Arduino Due
The Arduino Due is the first Arduino board based on a 32-bit RAM core microcontroller. With 54 digital input/output pins, 12 analog inputs.
More information about the Arduino Due controller can be found:
https://store.arduino.cc/usa/due

## Slide 12: 3-6 GHz RIS: Matlab Function set_latch()
2-bit phase shifter for each antenna and polarization
Use code “phase2decoder.m” to generate required 8-digit state code for all 72 elements from a pre-defined phase map
function: set_latch(Ard_obj, state_code_dec)
  Ard_obj: Arduino Due Object
  state_code_dec: 8-digit state code in decibel
Ant 1: V-pol
2-bit PS
Ant 1: H-pol
2-bit PS
Ant 2: V-pol
2-bit PS
Ant 2: H-pol
2-bit PS
Ant 1: V-pol
Ant 1: H-pol
Ant 2: H-pol
Ant 2: V-pol
bin2dec
state_code_dec(n) = 0-255
state_code_bin
Ant 1
Ant 2
D13
D12
D11
D10
D9
D8
D7
D6
Corresponding Arduino IO Pin

## Slide 13: 3-6 GHz RIS: Matlab Function pulse_decoder()
Arduino
Due
VCC
GND
USB
Digital I/O
Array Front View
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
69
70
71
72
68
67
Total 72 elements = (Element 1~8) + (Element 9~72)
Element 1-8 EN are controlled by a 3-to-8 decoder
Element 9-72 EN are controlled by a 6-to-64 decoder
function: pulse_decoder(Ard_obj, n)
  Ard_obj: Arduino Due Object
  n: element number
Corresponding Arduino IO Pin
Control bit | Explanation
D5 | 6-64: Address0
D4 | 6-64: Address1
D3 | 6-64: Address2
D2 | 6-64: Address3
D14 | 6-64: EN
D19 | 6-64: A
D20 | 6-64: B
D15 | 3-8: Address0
D16 | 3-8: Address1
D17 | 3-8: Address2
D18 | 3-8: EN
Please refer to the “pulse_decoder.m” code for detailed mapping

## Slide 14: 3-6 GHz RIS: Implementing Pre-defined Phase Map
Several things to note when implementing a pre-defined phase map
For example, we have a pre-defined phase map at f = 4.5 GHz and we set f0 = 3 GHz
A. Every element refer to the lowest phase value as 0 deg (i.e. every phase number should be positive)
B. The final phase map = pre-defined phase map / f * f0
C. Load the final phase map into “phase2decoder.m” with the configuration file “mixed_matrix_planewave_-20inc_test3.mat” and you will get the required state codes for all 72 elements in decibel
Example pre-defined phase map at 4.5 GHz

## Slide 15
Appendix: 2x2 Feed Array Specs

## Slide 16: 2x2 Feed Array
2x2 Patch Array
Front View
Back View
4mm spacer
1.7mm spacer
Upper Patch Board
Lower Patch Board
Feed Board
R1, R2, R4: 69.8 ohm
R3, R5, R6: 150 ohm
Side View

## Slide 17: 2x2 Feed Array: SMA RF Connector
142-0701-801 SMA 18GHz
Edge Launch Connector
Dimension of SMA Connector (142-0701-801)
More information can be found:
https://www.belfuse.com/resources/productinformations/cinchconnectivitysolutions/johnson/pi-ccs-john-142-0701-801.pdf

## Slide 18
End of Document